Download Steps:

- Go to: http://www.eas.asu.edu/~ptm/

- Select: Latest Models

- Download the required model from 130nm down to 22nm

- Save the Model card to: filename.m

- Open the file and change:

For NMOS: .model  nmos  nmos  level = 54 ( .model  ptmn65  bsim4  type=n

For PMOS: .model  pmos  pmos  level = 54 ( .model  ptmp65  bsim4  type=p

In order to simulate using the predictive technology models in cadence the following steps should be done:

- Copy the modified model files to the following directory: ("~/cadence/models/spectre").

- Generate Library (In Cadence Library Manager) and don't attach any technology at this time.

- Generate Cell with the schematic view.

- Insert either an nmos4 and/or pmos4 transistors from analogLib library.

- In the NMOS/PMOS object property menu set the Model Name parameter to ptmn65/ptmp65

- During the simulation phase if the simulator did not find the model files, you can attach the model files by:

  - In Analog Design Environment( Setup ( Model Libraries..

  - Attach the model files “don’t forget to press the ADD button”

Important notes:

    - You can use these model files with cadence version v5.0.33 or higher. On EESUN machines: source /usr/local/bin/setup.ic5033

    - The models are written to be used with the simulator spectre not spectreS